Network stack challenges
at increasing speeds
The 100Gbit/s challenge
Jesper Dangaard Brouer
Principal kernel Engineer
Red Hat inc.
Open Source Days, Feb 2016

---
Overview
- Understand 100Gbit/s challenge and time budget
  - Measurements: understand the costs in the stack?
- Recent accepted changes
  - TX bulking, xmit_more and qdisc dequeue bulk
- Memory allocator limitations
  - Extending SLUB with bulk API
- Future work needed
  - RX, qdisc, icache

---
Coming soon: 100 Gbit/s
- Increasing network speeds: 10G → 40G → 100G
  - challenge the network stack
- Rate increase, time between packets get smaller
  - Frame size 1538 bytes (MTU incl. Ethernet overhead)
    - at 10Gbit/s == 1230.4 ns between packets (815Kpps)
    - at 40Gbit/s == 307.6 ns between packets (3.26Mpps)
    - at 100Gbit/s == 123.0 ns between packets (8.15Mpps)
- Time used in network stack
  - need to be smaller to keep up at these increasing rates

---
Pour-mans solution to 100Gbit/s
- Recently got some 100Gbit/s NICs
  - If you don't, no problem:
    - use 10Gbit/s NICs with smaller frames
- Smallest frame size 84 bytes (due to Ethernet overhead)
  - at 10Gbit/s == 67.2 ns between packets (14.88Mpps)
- How much CPU budget is this?
  - Approx 201 CPU cycles on a 3GHz CPU
  - Approx 269 CPU cycles on a 4GHz CPU

---
100Gbit/s NICs do exist!
Thanks to Mellanox, now have 3x 100G NICs

---
Is this possible with hardware?
- Network stack bypass solutions
  - Grown over recent years
    - Like netmap, PF_RING/DNA, DPDK, PacketShader, OpenOnload etc.
    - RDMA and IBverbs avail in kernel, long time
- Have shown kernel is not using HW optimally
  - On same hardware platform
    - (With artificial network benchmarks)
    - Hardware can forward 10Gbit/s wirespeed smallest packet
      - On a single CPU !!!

---
Single core performance
- Linux kernel have been scaling with number of cores
  - hides regressions for per core efficiency
    - latency sensitive workloads have been affected
- Linux need to improve efficiency per core
  - IP-forward test, single CPU only 1-2Mpps (1000-500ns)
    - (Adding many cores Linux does scale up to 12Mpps)
  - Bypass alternatives handle 14.8Mpps per core (67ns)
    - although this is like comparing rockets and airplanes

---
Understand: nanosec time scale
- This time scale is crazy!
  - 67.2ns => 201 cycles (@3GHz)
- Important to understand time scale
  - Relate this to other time measurements
  - Next measurements done on
    - Intel CPU E5-2630 @2.3 GHz
    - Unless explicitly stated otherwise

---
Time-scale: cache-misses
- A single cache-miss takes: 32 ns
  - Two misses: 2x32=64ns
  - almost total 67.2 ns budget is gone
- Linux skb (sk_buff) is 4 cache-lines (on 64-bit)
  - writes zeros to these cache-lines, during alloc.
  - Fortunately not full cache misses
    - usually cache hot, so not full miss

---
Time-scale: cache-references
- Usually not a full cache-miss
  - memory usually available in L2 or L3 cache
  - SKB usually hot, but likely in L2 or L3 cache.
- CPU E5-xx can map packets directly into L3 cache
  - Intel calls this: Data Direct I/O (DDIO) or DCA
- Measured on E5-2630 (lmbench command "lat_mem_rd 1024 128")
  - L2 access costs 4.3ns
  - L3 access costs 7.9ns
  - This is a usable time scale

---
Time-scale: "LOCK" operation
- Assembler instructions "LOCK" prefix
  - for atomic operations like locks/cmpxchg/atomic_inc
  - some instructions implicit LOCK prefixed, like xchg
- Measured cost
  - atomic "LOCK" operation costs 8.23ns (E5-2630)
    - Between 17-19 cycles (3 different CPUs)
- Optimal spinlock usage lock+unlock (same single CPU)
  - Measured spinlock+unlock calls costs 16.1ns
    - Between 34-39 cycles (3 different CPUs)
[Speaker Notes: E5-2630 @ 2.30GHz locked cmpxchg:18 cycles(tsc) 8.23 ns spin_lock+unlock: 39 cycles(tsc) 17.213 ns Div2: 19.5 cycles – 8.60ns E5-2695 @ 2.8GHz locked cmpxchg: 19 cycles(tsc) 7.86 ns spin_lock+unlock: 34 cycles(tsc) 13.944 ns Div2: 17 cycles - 6.97ns I7-4790K CPU @ 4.00GHz locked cmpxchg: 17 cycles(tsc) 4.33 ns spin_lock+unlock: 38 cycles(tsc) 9.637 ns Div2: 19 cycles - 4.82ns]

---
Time-scale: System call overhead
- Userspace syscall overhead is large
  - (Note measured on E5-2695v2)
  - Default with SELINUX/audit-syscall: 75.34 ns
  - Disabled audit-syscall: 41.85 ns
- Large chunk of 67.2ns budget
- Some syscalls already exists to amortize cost
  - By sending several packet in a single syscall
    - See: sendmmsg(2) and recvmmsg(2) notice the extra "m"
    - See: sendfile(2) and writev(2)
    - See: mmap(2) tricks and splice(2)

---
Time-scale: Sync mechanisms
- Knowing the cost of basic sync mechanisms
  - Micro benchmark in tight loop
- Measurements on CPU E5-2695
  - spin_{lock,unlock}:	34 cycles(tsc) 13.943 ns
  - local_BH_{disable,enable}:	18 cycles(tsc) 7.410 ns
  - local_IRQ_{disable,enable}:	7 cycles(tsc) 2.860 ns
  - local_IRQ_{save,restore}:	37 cycles(tsc) 14.837 ns
- Notice: IRQ-save/restore cost more than spin_lock

---
Main tools of the trade
- Out-of-tree network stack bypass solutions
  - Like netmap, PF_RING/DNA, DPDK, PacketShader, OpenOnload, etc.
- How did others manage this in 67.2ns?
  - General tools of the trade is:
    - batching, especially TX batching to HW queues
    - preallocation, prefetching,
    - staying cpu/numa local, avoid locking,
    - shrink meta data to a minimum, reduce syscalls,
    - faster cache-optimal data structures
    - lower instruction-cache misses

---
Batching is a fundamental tool
- Challenge: Per packet processing cost overhead
  - Use batching/bulking opportunities
    - Where it makes sense, avoid introduce latency
    - Possible at many different levels
- Simplified explanation: How to increase time budget
  - Remove per packet processing overhead
  - E.g. processing 10 packets in a bundle/batch
    - 67.2 ns = 672 ns time between 10 pkt bundles
    - 201 cycles => 2010 cycles

---
Recent changes
What has been done recently

---
Unlocked Driver TX potential
- Pktgen 14.8Mpps single core (10G wirespeed)
  - Spinning same SKB (no mem allocs)
    - Avail since kernel v3.18-rc1
- Primary trick: Bulking packet (descriptors) to HW
- What is going on: MMIO writes
  - Defer tailptr write, which notifies HW
    - Very expensive write to non-cacheable mem
  - Hard to perf profile
    - Write to device
      - does not showup at MMIO point
      - Next LOCK op is likely “blamed”

---
How to use new TX capabilities?
- Next couple of slides
  - How to integrate new TX capabilities
    - In a sensible way in the Linux Kernel
    - e.g. without introducing latency

---
Intro: xmit_more API toward HW
- SKB extended with xmit_more indicator
  - Stack use this to indicate (to driver)
  - another packet will be given immediately
    - After/when ->ndo_start_xmit() returns
- Driver usage
  - Unless TX queue filled
  - Simply add the packet to HW TX ring-queue
  - And defer the expensive indication to the HW
- When to “activate” xmit_more?

---
Challenge: Bulking without added latency
- Hard part:
  - Use bulk API without adding latency
- Principal: Only bulk when really needed
  - Based on solid indication from stack
- Do NOT speculative delay TX
  - Don't bet on packets arriving shortly
  - Hard to resist...
    - as benchmarking would look good
    - Like DPDK does...

---
Use SKB lists for bulking
- Changed: Stack xmit layer
  - Adjusted to work with SKB lists
  - Simply use existing skb→next ptr
- E.g. See dev_hard_start_xmit()
  - Skb→next ptr simply used as xmit_more indication
- Lock amortization
  - TXQ lock no-longer per packet cost
  - dev_hard_start_xmit() send entire SKB list
  - while holding TXQ lock (HARD_TX_LOCK)

---
Existing aggregation in stack GRO/GSO
- Stack already have packet aggregation facilities
  - GRO (Generic Receive Offload)
  - GSO (Generic Segmentation Offload)
  - TSO (TCP Segmentation Offload)
- Allowing bulking of these
  - Introduce no added latency
- Xmit layer adjustments allowed this
  - validate_xmit_skb() handles segmentation if needed

---
Qdisc layer bulk dequeue
- A queue in a qdisc (Linux Traffic Control)
  - Very solid opportunity for bulking
    - Already delayed, easy to construct skb-list
- Rare case of reducing latency
  - Decreasing cost of dequeue (locks) and HW TX
    - Before: a per packet cost
    - Now: cost amortized over packets
- Qdisc locking have extra locking cost
  - Due to __QDISC___STATE_RUNNING state
  - Only single CPU run in dequeue (per qdisc)

---
Choice: Qdisc TX bulk require BQL
- Only support qdisc bulking for BQL drivers
  - Implement BQL in your driver now!
    - BQL – Byte Queue Limit
- Needed to avoid overshooting NIC capacity
  - Overshooting cause requeue of packets
- Current qdisc layer requeue cause
  - Head-of-Line blocking
  - Future: better requeue in individual qdiscs?
- Extensive experiments show
  - BQL is very good at limiting requeue's

---
FIB lookup and other optimizations
- IP-forwarding route lookups
  - FIB lookup (were) most expensive component
  - Alex Duyck improved this recently!
- Lookout for Alex Duyck's optimizations e.g.:
  - Low level eth_proto_is_802_3 optimized
  - Page frag alloc cache generalized and optimized
    - See __alloc_page_frag()
  - Finer grained barriers in drivers (dma_wmb/dma_rmb)

---
Summary: Linux perf improvements
- Linux performance, recent improvements
  - approx past 2 years:
- Lowest TX layer (single core, pktgen):
  - Started at: 4 Mpps → 14.8 Mpps (← max 10G wirespeed)
- Lowest RX layer (single core):
  - Started at: 6.4 Mpps → 12 Mpps (still experimental)
- IPv4-forwarding
  - Single core: 1 Mpps → 2 Mpps
  - Multi core : 6 Mpps → 12 Mpps (RHEL7.2 benchmark)

---
Future work
- What needs to be worked on?
  - Large subject, more details at NetDev 1.1 (in Seville next week)
    - Network Performance BoF
- Current stack limited by
  - Taking advantage of TX capabilities
  - RX performance/limitations (DMA or mem alloc limits?)
  - Qdisc “baseline” overhead
  - Memory allocator, hitting slowpath
  - Instruction cache misses, forward case

---
What about RX?
- TX looks good now: How do RX perform?
  - Remember: 100Gbit/s big 1500 byte frames = 8.15Mpps
- Evaluate lowest RX layer, with 100G driver
  - Simply drop packet in driver on RX, single core
    - Disappointed to only see 6.4Mpps
  - Optimized driver to: RX driver drop: 12Mpps → 82.7 ns
    - Avoid cache miss on eth_trans_type() + icache RX loop
    - +using SLUB bulk free SKB API, + tuning SLUB allocator
  - What is max performance from this layer?:
    - Extrapolated: 19 Mpps as max performance (single core)
      - Subtract, SLUB (7.3 ns) and SKB (22.9 ns) related → 52.5 ns

---
Instruction Cache misses
- Packet forward case
  - Too slow, when calc/add components
    - IP-forward 1Mpps → 1000ns
    - Tuned IP-forward 2Mpps → 500ns
  - Profiling shows many inst-cache misses
    - Better fwd performance with new GCC compilers
      - Measured factor x10 reduced icache-misses
  - Code level icache optimizations
    - Make stack work in “stages”
    - Driver bulking on RX
      - Small RX queue, before activating stack call loop
    - Do more in GRO layer, and for RPS

---
Optimize memory allocator
- Identified memory alloc bottleneck
  - Network stack is hitting MM/slab slowpath
    - Optimizing this was challenging work
- Well, almost done!
  - Bulk alloc and free API (slab/kmem_cache)
    - API accepted into kernel 4.3
    - Optimizations to appear in kernel 4.4
  - Network stack usage
    - Posted: http://thread.gmane.org/gmane.linux.network/384302/
      - Likely appear in next kernel release

---
Memory Allocator limitations
- Artificial RX benchmark (Drop packets early)
  - Don't see real limitations of mem alloc
- Real network stack usage, hurts allocator
    1. RX-poll alloc up-to 64 packets (SKBs)
    2. TX put packets into TX ring
    3. Wait for TX completion, free up-to 256 SKBs
- Above cause
  - IP-forward to hit “slowpath” for SLUB

---
Latest work: SLUB bulking is fast!
- Optimizing SLUB allocator (patchset V4 accepted)
  - Bulk alloc + free cost (CPU i7-4790K @4GHz)
    - SLUB fastpath: 42 cycles(tsc) / slowpath: 105 cycles
    - Hitting: fastpath of SLUB
      - SLUB bulk	x1 →	49 cycles(tsc)
      - SLUB bulk	x2 →	30 cycles(tsc)
      - SLUB bulk	x4-16 →	20 – 17 cycles
      - (below net stack use-case) my latest perf improvements!
      - SLUB bulk	x32-64	→ 18 – 23 cycles
      - SLUB bulk	x128-250	→ 27 – 37 cycles
    - Notice: faster than single object “fastpath”!!!

---
Qdisc path overhead
- Qdisc code path takes 6 LOCK ops
  - LOCK cost on this arch: approx 8 ns
  - 8 ns * 6 LOCK-ops = 48 ns pure lock overhead
- Measured qdisc overhead: between 58ns to 68ns
    - 58ns: via trafgen –qdisc-path bypass feature
    - 68ns: via ifconfig txlength 0 qdisc NULL hack
  - Thus, using between 70-82% on LOCK ops
- Dequeue side lock cost, now amortized
  - But only in-case of a queue
  - Empty queue, “direct_xmit” still see this cost
  - Enqueue still per packet locking
[Speaker Notes: In the qdisc optimal "fast-path" where the qdisc is empty, the following locking occurs :: In __dev_xmit_skb(): (1) spin_lock(root_lock) (detect qdisc empty, allow direct xmit) calling sch_direct_xmit() In sch_direct_xmit(): (2) spin_unlock(root_lock) In sch_direct_xmit(): (3) HARD_TX_LOCK(dev, txq, smp_processor_id()); In sch_direct_xmit(): (4) HARD_TX_UNLOCK(dev, txq); In sch_direct_xmit(): (5) spin_lock(root_lock); Return to __dev_xmit_skb(): (6) spin_unlock(root_lock);]

---
Future: Lockless qdisc
Motivation for lockless qdisc (cmpxchg based)
  1. Direct xmit case (qdisc len==0) “fast-path”
    - Still requires taking all 6 locks!
  1. Enqueue cost reduced (qdisc len > 0)
    - from 16ns to 10ns
- Measurement show huge potential for saving
  - (lockless ring queue cmpxchg base implementation)
  - If TCQ_F_CAN_BYPASS saving 58ns
    - Difficult to implement 100% correct
  - Not allowing direct xmit case: saving 48ns

---
Future: “packet-page” level
- General consensus at NetDev BoF
- Add layer in driver before SKB allocation
  - Pickup raw packet page from NIC RX ring
  - Allow some hook, use-cases
    - e.g. run eBPF filter directly on raw packet page
      - Drop packet (expecting) wirespeed (recycle page quickly)
    - e.g. faster tcpdump point
    - e.g. hook for netmap/DPDK
      - Tricky: due to isolation and security aspects

---
The End
- Most of these changes are avail in RHEL7.2
  - Linux multi-core IPv4-routing scales to 12Mpps
    - (RHEL7.1) 6Mpps → (RHEL 7.2) 12Mpps
      - Lookup Alex Duyck talk from LinuxCon2015
- Future changes see: Network Performance BoF
  - In Seville, at NetDev 1.1
    - LWN article https://lwn.net/Articles/676806/
    - YouTube: https://www.youtube.com/watch?v=5eWmExBxidA
  - All about how to fix/improve the kernel network stack
  Questions?

---
Extra
Extra slides

---
Micro benchmark: kmem_cache
- Micro benchmarking code execution time
  - kmem_cache with SLUB allocator
- Fast reuse of same element with SLUB allocator
  - Hitting reuse, per CPU lockless fastpath
  - kmem_cache_alloc+kmem_cache_free = 19ns
    - 42-48 cycles(tsc)
- Pattern of 256 alloc + 256 free (Based on ixgbe cleanup pattern)
  - Cost increase to: 40ns
    - 88-105 cycles

---
Qmempool: Faster caching of SKBs
- Implemented qmempool (Dec 2014)
  - Lock-Free bulk alloc and free scheme
    - Backed by alf_queue
- Practical network measurements show
  - saves 12 ns on "fast-path" drop in iptables "raw" table
  - saves 40 ns with IP-forwarding
    - Forwarding hits slower SLUB use-case

---
Qmempool: Micro benchmarking
- Micro benchmarked against SLUB
  - Cost of alloc+free (CPU i7-4790K @4GHz)
- Fast-path: reuse-same element in loop
  - kmem_cache(slub):	42 cycles(tsc)
  - qmempool in softirq:	31 cycles(tsc)
  - qmempool BH-disable:	44 cycles(tsc)
- Slower-path: alloc 256-pattern before free:
  - kmem_cache(slub):	105 cycles(tsc)
  - qmempool BH-disable:	58 cycles(tsc)

---
Qmempool what is the secret?
- Why is qmempool so fast?
  - Primarily the bulk support of the Lock-Free queue
  - Sharedq MPMC bulk elems out with a single cmpxchg
    - thus, amortize the per elem cost
- Currently uses per CPU SPSC queue
  - requires no lock/atomic operations
    - could be made faster with a simpler per CPU stack

---
Alf_queue building block for qmempool
- The ALF (Array based Lock-Free) queue
  - (Basic building for qmempool)
  - Killer feature is bulking
  - Lock-Free ring buffer, but uses cmpxchg ("LOCK" prefixed)
  - Supports Multi/Single-Producer/Consumer combos.
  - Cache-line effect also amortize access cost
    - 8 pointers/elems per cache-line (on 64bit)
  - Pipeline optimized bulk enqueue/dequeue
    - (pipelining currently removed in upstream proposal, due to code size)
- Basically "just" an array of pointer used as a queue
  - with bulk optimized lockless access

---
Qmempool purpose: PoC
- Rejected upstream!
- Practical implementation, to find out:
  - if it was possible to be faster than kmem_cache/slub
- Provoke MM-people
  - To come up with something just-as-fast
  - Integrate ideas into MM-layer
  - Perhaps extend MM-layer with bulking
- Next: SLUB fastpath improvements
  - and potential booster shots through bulk alloc and free

---
Extra: pktgen stack bench
- Recent: pktgen inject packet into stack
  - Useful for localhost bench without HW
  - See script: pktgen_bench_xmit_mode_netif_receive.sh
    - Default usage mode: Very early ingress drop in ip_rcv()
      - 52,502,335pps → 19ns (spinning same SKB)
    - Usage: Measures SKB memory allocator performance
      - Param “-b 0” disable burst, same drop point
      - 7,206,871pps → 139ns (CPU i7-4790K @ 4.00GHz)
      - Difference: 120ns – too much other stuff
        - Pktgen own overhead 30% (approx 42ns)
        - 9.71% __build_skb (13.5ns)
        - 10.82% __netdev_alloc_skb+__{free,alloc}_page_frag (15ns)
        - 6.83% kmem_cache_alloc+free (9.5ns) → close to bench=10.814ns
        - 4.55% ktime_get_with_offset+read_tsc (6.3ns) → strange PTP module

---
Extra: Smarter clearing of SKBs
- Clearing SKB is expensive
  - __build_skb() 40% spend in memset
    - Translates into asm: rep stos
    - Startup cost 15 cycles
      - Suspect CPU stall/pipeline stall?
- Find smarter clearing or reduce SKB size?

---
Extra: cost of clear SKB
SKB “clear” 200 Bytes, SLAB object 256 Bytes (CPU i7-4790K @ 4.00GHz)
Note	Bytes-to-clear	Cycles	Cycles per 256B
Hand-optimized	200	26
Rep-stos	200	36
Hand-optimized	256	32
Rep-stos	256	43
Below: rep-stos	512	72	36.00
3x 256	768	46	15.30
4x	1024	49	12.25
5x	1280	53	10.60
6x	1536	60	10.00
8x	2048	75	9.38
16x	4096	134	8.38
32x	8192	255	7.97

---
Qdisc locking is nasty
- Always 6 LOCK operations (6 * 8ns = 48ns)
  - Lock qdisc(root_lock) (also for direct xmit case)
    - Enqueue + possible Dequeue
      - Enqueue can exit if other CPU is running deq
      - Dequeue takes __QDISC___STATE_RUNNING
  - Unlock qdisc(root_lock)
  - Lock TXQ
    - Xmit to HW
  - Unlock TXQ
  - Lock qdisc(root_lock) (can release STATE_RUNNING)
    - Check for more/newly enqueued pkts
      - Softirq reschedule (if quota or need_sched)
  - Unlock qdisc(root_lock)

---
MM: Derived MM-cost via pktgen
- Hack: Implemented SKB recycling in pktgen
  - But touch all usual data+skb areas, incl. zeroing
- Recycling only works for dummy0 device:
  - No recycling: 3,301,677 pkts/sec = 303 ns
  - With recycle: 4,424,828 pkts/sec = 226 ns
- Thus, the derived Memory Manager cost
  - alloc+free overhead is (303 - 226): 77ns
  - Slower than expected, should have hit slub fast-path
    - SKB->data page is likely costing more than SLAB

---
MM: Memory Manager overhead
- SKB Memory Manager overhead
  - kmem_cache: between 19ns to 40ns
    - Between: 42-105 cycles
  - pktgen fastpath recycle derived: 77ns
    - (77-19) = 58ns data/page + “touch” overhead?
  - Larger than our time budget: 67.2ns
- Thus, for our performance needs
  - Either, MM area needs improvements
  - Or need some alternative faster mempool

---
Extra: Comparing Apples and Bananas?
- Comparing Apples and Bananas?
  - Out-of-tree bypass solution focus/report
    - Layer2 “switch” performance numbers
    - Switching basically only involves:
      - Move page pointer from NIC RX ring to TX ring
  - Linux bridge
    - Involves:
      - Full SKB alloc/free
      - Several look ups
      - Almost as much as L3 forwarding

---
General purpose network platform
- For general purpose networking
  - Linux Kernel is best platform available
- But needs to rethink its architecture
  - To adapt for future high-end network performance challenges

---
HW level TX batching
- Batch packets into ixgbe drivers HW TX ring buffer
  - update TDT (Transmit Descriptor Tail) every N packets
- Pktgen showed significant perf improvement
  - Tuning pktgen to send 7Mpps (single CPU)
  - Update TDT every 32 packets, result 11Mpps
    - (2x=9Mpps, 4x9.6Mpps, 8x=10.5Mpps, 16x=10.9Mpps)
- Thus, ixgbe hardware level batching worth doing
  - Solution that does not increase latency, hard part

---
Using TSQ
- TCP Small Queue (TSQ)
  - Use queue build up in TSQ
    - To send a bulk xmit
      - To take advantage of HW TXQ tail ptr update
    - Should we allow/use
      - Qdisc bulk enqueue
        - Detecting qdisc is empty allowing direct_xmit_bulk?