Jimit Mahadevia (jimit@elitecore.com)
Nishit Shah (nishit@elitecore.com)
This work is licensed under a Creative Commons Attribution-Share Alike 3.0 Unported License

---
Introduction
Introduction
Topics cover in presentation are,
Netfilter Architecture
Netfilter Functionality
Packet Traversal through Netfilter
Real-Time examples of Packet Traversal.
Packet Traversal through Linux Kernel Network Stack(combined with Netfilter)

---
Netfilter Architecture
Netfilter Architecture
Netfilter is a framework inside Linux 2.4.x and 2.6.x kernel series that intercepts network traffic at various predefined points (i.e. hooks) in network protocol stack and facilitates,
Packet Filtering
Packet Mangling.
Stateless/Stateful Firewalling
Network Address Translation (NAT)

---
Netfilter Architecture
The Hooks
Hooking is a programming technique to make a chain of procedures as a handler.

---
Netfilter Architecture
The Hooks
Unregistering the hook means setting the original procedure as the event handler.
Hooking can be used for many purposes including debugging and extending original functionality, but also misused to inject (potentially malicious) code to the event handler

---
Netfilter Architecture
Netfilter Hooks
There are five netfilter hooks defined in IPv4
PRE_ROUTING
LOCAL_IN
FORWARD
LOCAL_OUT
POST_ROUTING

---
Netfilter Architecture
Netfilter Hooks
Route
Route
LOCAL PROCESS
PRE
IN
FWD
OUT
POST

---
Netfilter Architecture
Netfilter Hooks
PRE_ROUTING HOOK
  - This hook is before routing decision is to be made. Thus all actions that is to be taken on packet before routing can be done by registering to this hook.
LOCAL_IN HOOK
  - All packets which are destined for local system can be accessed by registering to this hook.
FORWARD HOOK
  - All packets which are not for local system and which are forwarded can be accessed by registering to this hook.

---
Netfilter Architecture
Netfilter Hooks
LOCAL_OUT HOOK
  - All packets which are generated by local system can be accessed by registering to this hook.
POST_ROUTING HOOK
  - All packets going out from system(local and forwarded) can be accessed by registering to this hook.

---
Netfilter Architecture
Netfilter Hooks
Kernel modules can register to listen at any of these hooks.
Registration includes a callback function of kernel module,priority of module to be called etc.
When netfilter hook is called from the core networking code, each module registered at that point is called by calling callback function in the order of priorities, and is free to manipulate the packet. The module can then tell netfilter to do one of five things:
NF_ACCEPT: continue traversal as normal.
NF_DROP: drop the packet; don't continue traversal.

---
Netfilter Architecture
Netfilter Hooks
NF_STOLEN: I've taken over the packet; don't continue traversal.
NF_QUEUE: queue the packet (usually for userspace handling).
NF_REPEAT: call this hook again.

---
Packet Filtering
Packet Filtering System is implemented on top of Netfilter Framework.
Packet Filtering System is used to filter packets based on various matching criteria like source/destination IP, source/destination ports, protocols, IP/TCP/UDP/ICMP header fields, connection states etc.

---
Packet Filtering
Kernel module of Packet Filtering System is registered with Netfilter & capable of doing actual packet filtering based on various criteria.
Packet Filtering System registered itself at following Netfilter Hooks
  - LOCAL_IN, FORWARD, LOCAL_OUT
Iptables userspace tool is used to give packet filtering rules to kernel module of packet filtering system . Packet filtering rules are consist of,
Insertion Point
Insertion Order
one or more matching criteria.
Single Target to specify Action.

---
Packet Filtering System in Netfilter Hooks
Route
Route
LOCAL PROCESS
PRE
IN
FWD
OUT
POST

---
Packet Mangling
Packet Mangling System is implemented on top of Netfilter Framework.
It allows you to mangle packet information.
Gives you the ability to a multitude of possibilities
Example Usages
Strip All IP Options
Change TOS value
Change TTL value
Clamp MSS to PMTU
Mark packets within kernel

---
Packet Mangling
Kernel module of Packet Mangling System is registered with Netfilter & capable of doing actual packet mangling based on various criteria.
Packet Mangling System registered itself at following Netfilter Hooks
  - PRE_ROUTING, LOCAL_IN, FORWARD, LOCAL_OUT, POST_ROUTING
Iptables userspace tool is used to give packet mangling rules to kernel module of packet mangling system. Packet mangling rules are consist of,
Insertion Point
Insertion Order
one or more matching criteria.
Single Target to provide mangling information.

---
Packet Mangling System in Netfilter Hooks
Route
Route
LOCAL PROCESS
PRE
IN
FWD
OUT
POST

---
Connection Tracking
Connection Tracking or conntrack is implemented on top of Netfilter Framework
It keeps track about all currently ongoing connections in which the local machine is involved.
This state information about connections is to be used by several other linux kernel modules like,
NAT System
Any module that implements stateful firewalling

---
Connection Tracking
Packet Fields involved in Connection Tracking
Connection Tracking System has to inspect some fields or couple of fields of a packet for connection tracking of individual connections.
These fields are dependent on protocol and may vary from protocol to protocol.
For TCP
Source IP Address, Source Port, Destination IP Address, Destination Port, TCP flags will be used.
Thus Conntrack use above information from a TCP packet to track connection. First four fields will be used to identify the connection and last field is used to track the connection. It also uses advance tracking with sequence number, acknowledgment number and window size.

---
Connection Tracking
For UDP
Source IP Address, Source Port, Destination IP Address, Destination Port will be used.
For ICMP
Source IP Address, ICMP TYPE, ICMP Code, ICMP ID will be used.
Generic Protocols
Source IP,Destination IP, Protocol will be used.

---
Connection Tracking
Connection Tracking System keeps connection related information like:
Source/Destination IP
Protocol Number (TCP,UDP.ICMP etc..)
Source/Destination Port (if any)
Current State of connection(if any)
Sequence Number , Ack number & Window Size (TCP Only)
No. of packets/bytes transmitted over connection
Duration, etc.

---
Connection Tracking
For each packet entering the system, conntrack will try to find the connection information this packet belongs to, at the PRE_ROUTING hook with highest priority.
Any other kernel module after this point can use this tracking information.
For example, This information is used in iptables rule that enables filtering/Mangling based on the packet's state.

---
Connection Tracking
Using Connection Tracking Information(I.e connection state), there are following Userland states possible,
  - New
  - ESTABLISHED
  - RELATED
  - INVALID

---
Connection Tracking
NEW
The NEW state tells us that the packet is the first packet that we see. This means that the first packet that the conntrack module sees, within a specific connection.
For example, if we see a SYN packet and it is the first packet in a connection that we see, state is NEW.
However, the packet may as well not be a SYN packet and still be considered NEW. This may lead to certain problems in some instances, but it may also be extremely helpful when we need to pick up lost connections from other firewalls, or when a connection has already timed out, but in reality is not closed.

---
Connection Tracking
ESTABLISHED
The ESTABLISHED state has seen traffic in both directions.
ESTABLISHED connections are fairly easy to understand. The only requirement to get into an ESTABLISHED state is that one host sends a packet, and that it later on gets a reply from the other host.
The NEW state will upon receipt of the reply packet to or through the firewall change to the ESTABLISHED state.	ICMP reply messages can also be considered as ESTABLISHED, if we created a packet that in turn generated the reply ICMP message

---
Connection Tracking
RELATED
The RELATED state is one of the more tricky states. A connection is considered RELATED when it is related to another already ESTABLISHED connection.
What this means, is that for a connection to be considered as RELATED, we must first have a connection that is considered ESTABLISHED. The ESTABLISHED connection will then spawn a connection outside of the main connection.
The newly spawned connection will then be considered RELATED, if the conntrack module is able to understand that it is RELATED.
The RELATED state will upon receipt of the reply packet to or through the firewall change to the ESTABLISHED state

---
Connection Tracking
RELATED (Continued…)
Some examples of connection that can be considered as RELATED are,
The FTP-data connections that are considered RELATED to the FTP control port.
ICMP error messages in reply of IP packets
Thus RELATED could be used to allow ICMP error messages, FTP transfers etc. to work properly through the stateful firewall.
Note that most TCP protocols and some UDP protocols that rely on this mechanism are quite complex and send connection information within the payload of the TCP or UDP data segments, and hence require special helper modules to be correctly understood

---
Connection Tracking
INVALID
The INVALID state means that the packet can't be identified or that it does not have any state.
This may be due to several reasons, such as the system running out of memory or ICMP error messages that do not respond to any known connections.
Generally, it is a good idea to DROP everything in this state.

---
Connection Tracking
Connection Tracking System also maintains various states of a connection in kernel modules.
Userland states and Kernelland states are different.
Kernelland states are vary from protocol to protocol
Each Kernelland state has its timeout value. It means if some connection is in particular state and nothing happens on that connection than after timeout value connection entry get destroyed.

---
Connection Tracking
Various Kernelland states and timeouts for TCP
State
Timeout value
NONE
30 minutes
ESTABLISHED
5 days
SYN_SENT
2 minutes
SYN_RECV
60 seconds
FIN_WAIT
2 minutes
TIME_WAIT
2 minutes
CLOSE
10 seconds
CLOSE_WAIT
12 hours
LAST_ACK
30 seconds
LISTEN
2 minutes

---
Connection Tracking
Various Kernelland states and timeouts for UDP
UDP connections are in themselves not stateful connections, but rather stateless.
Thus here no such Kernelland states, but still timeout for connection tracking entries are as follows.
If Connection Tracking sees UDP packets in only one direction, timeout is 30 seconds.
If Connection Tracking sees UDP packets in both directions, timeout is 180 seconds.

---
Connection Tracking
Various Kernelland states and timeouts for ICMP
ICMP packets are far from a stateful stream, since they are only used for controlling and should never establish any connections
Thus here no such Kernelland states, but still timeout for connection tracking entries are as follows
If Connection Tracking sees ICMP packets in only one direction, timeout is 30 seconds.
In case of ICMP after ICMP reply there will be absolutely no more legal traffic, thus connection entry is destroyed immediately.

---
Connection Tracking
Kernel module of Connection Tracking is registered with Netfilter & capable of doing connection tracking
Connection Tracking System consist of Framework of adding connection traacking modules for various protocols (I.e TCP,ICMP,UDP,Generic,GRE etc..)
Connection Tracking System registered itself at following Netfilter Hooks
  - PRE_ROUTING, LOCAL_IN, LOCAL_OUT, POST_ROUTING

---
Connection Tracking in Netfilter Hooks
Route
Route
LOCAL PROCESS
PRE
IN
FWD
OUT
POST

---
NAT
NAT System is implemented on top of Netfilter Framework.
NAT means rewriting packet source and/or destination addresses/ports.
One can divide NAT into following:
1) SNAT: causes the packet's source address (& optionally port) to be rewritten.
MASQUERADE: is a special, restricted form of SNAT. The source IP address is NATed to by looking at the IP address of the outgoing interface.

---
NAT
2.) DNAT: causes the packet's destination address (& optionally port) to be rewritten.
REDIRECT: is a special, restricted form of DNAT. The destination IP address is NATed to by looking at the IP address of the incoming interface
NAT requires Connection Tracking System to keep states and expectations

---
NAT
Kernel module of NAT is registered with Netfilter & capable of doing actual packet NAT based on various criteria.
NAT registered itself at following Netfilter Hooks
  - PRE_ROUTING (for destination NAT)
  - For Traffic Entering into System
  - LOCAL_OUT (for destination NAT)
  - For Traffic Originating from System
  - LOCAL_IN (for Source NAT)
  - For Traffic destinated to System
  - POST_ROUTING (for Source NAT)
  - For Traffic destinated to other System

---
NAT
Iptables userspace tool is used to give NAT rules to kernel module of NAT System. NAT rules are consist of,
Insertion Point
Insertion Order
one or more matching criteria.
Single Target to provide NAT information.

---
NAT in Netfilter Hooks
Route
Route
LOCAL PROCESS
PRE
IN
FWD
OUT
POST

---
THANK YOU
THANK YOU